## Slide 1: Phased Arrays – An Introduction
  Emeritus Prof Doug Gray,
  University of Adelaide
Key References :
H.L. van Trees “Optimum Array Processing”
C.W. Therrien “Discrete Random Signals and Statistical Signal Processing”
Unpublished notes “Beamforming and Array Processing”

## Slide 2: Adelaide – South Australia

## Slide 3: Course Outline
Day 1
  Concepts, key issues, signal representation and propagation
  Arrays, Beamforming and Beam patterns
  - beamwidths, sidelobes and grating lobes, array shading
  Multiple beams : Time domain and frequency beamforming
Day 2
  Beamforming random signals - cross-spectral matrices
  Optimum beamforming in frequency domain
  Sample matrix inverse – SMI beamforming
  Subspace methods – Music and Beam Space
Day 3
  Space-time domain adaptive – STAP
  Gradient descent, LMS – adaptive beamforming
  STAP examples – radar and GPS
  MIMO radar

## Slide 4: Mechanical vs electronic scanning
Mechanical scanning
– typically a rotating antenna with its beam
formed at broadside
- various antenna types
various scan patterns but long revisit times
ESA Electronically steered antenna arrays
– typically (but not always) a fixed array of separate antennas
Beamsteering
  amplitude and phase control for each antenna
scanning by variation of the phase shifts

## Slide 5: An Early Array

## Slide 6: Some phased arrays
6

## Slide 7: Phased Array Weather Radars
7
NWRT National Weather Radar Testbed - Norman Oklahoma
Aegis SPY-1A radar S-band
  pulse to pulse beamsteering capability
    storm evolution, beam multiplexing, dual use,
    spaced antenna interferometry, monopulse,
    atmospheric refractivity, microbursts
CASA Collaborative Adaptive Sensing of the Atmosphere
Phase tilt array panels
electronically steer in azimuth
mechanically in elevation
X band, Dual polarimetric
Developed at UMass/Raytheon
Now built by First RF
Deployed in Adelaide for bushfire monitoring

## Slide 8
Airborne Fire Control and Tracking Radar Example
Active Electronically Scanned Array
Major radar upgrade for the U.S. Air Force F-15C aircraft
Increases pilot situational awareness
Enhanced multi-target tracking
Features upgraded identification-friend-or-foe and environmental control systems
Can simultaneously guide multiple missiles to several targets widely spaced in azimuth, elevation, or range.

## Slide 9: Over the Horizon HF Radar Array

## Slide 10: CEA-FAR Active Phased Array Radar
CEA-FAR Multi-function Radar
  S-Band (~3GHz)
  Active Phased Array
  3D beamforming

## Slide 11
Ground based Surveillance or Early Warning Radar Example
Peak Power 1,792 active elements at 325 watts = 582.4 kilowatts (kW)
Duty Factor 25% (11% search, 14% track)
Average Power 145.6 kW
Effective Transmit Gain 37.92 decibel (dB)
Active Radar Diameter 22.1 meters
Frequency 420 megahertz (MHz) to 450 MHz
Radar Detection Range 5,556 kilometers (3,000 nautical miles)
Wavelength 0.69 meters at 435 MHz
Sidelobes -20 dB (first), -30 dB (second),
-38 dB (root mean square)
Face Tilt 20 degrees
Number of Faces 2
3 dB Beam Width 2.2 degrees

## Slide 12: Synthetic Aperture Radar
R

## Slide 13: Sonobuoy Array

## Slide 14: Radio-Astronomy Array

## Slide 15: GPS Array

## Slide 16: Slotted Waveguide – Not a Phased Array

## Slide 17: Phased Arrays Advantages
Independent control of amplitude and phase
Less radiating power per element – transmit power distributed
Rapid scan – extreme agility
Ability to dwell on particular targets
Reduced weight
Control of beampattern
Reduced RCS
Distributed failure
– graceful degradation
Clutter mitigation

## Slide 18: Phased Arrays Disadvantages
Grating lobes
Spacing less than l/2
Mutual coupling
    Degradation of beam pattern
    Blind angles
    Different at edges
More complex
  Beamwidth and gain change with look angle
  60 degree sector
  Beam stabilisation required
  Element calibration required
  Off boresight polarimetry issues
From Stimson

## Slide 19: Systems Aspects - sonar

## Slide 20: Radar System Perspective
Generate Transmit Signal waveform
Up-convert to transmit frequency
Isolate transmit and receive signals
Antenna or phased array
Signal propagates to scatterers
Signal
scattered by
target
Clutter
Jamming
Detection
Integration
CFAR
Tracking
Localisation
Classification
Signal Processing
Doppler processing
Range processing
Beamform on receive
Receiver Hardware
Antenna or phased array